## Slide 1: Digital Voltmeter Using Arduino and LCD Display
Presented by Group 1

## Slide 2: Executed by:
202516060 - Abdullah Al Kafi
202516067 - Mst. Sanjana Afrin Tanha
202516071 - Hasin Ishraq Khan
202516073 - Muhammad Labib Daiyan Bhuiyan
202516077 - Md. Rowshon Jamil Anondo

## Slide 3: Table of Content:
Prologue
Circuit Components
Circuit Diagram
Code
Mechanism
Results and Applications

## Slide 4: Prologue
What is a voltmeter? A voltmeter (or multimeter in voltage mode) is an instrument used to measure the potential difference between two points in a circuit.
How was it built in this project? A voltage divider circuit uses two resistors connected in series across a voltage source. The output voltage is taken from the junction of the resistors, which provides only a fraction of the input voltage based on the resistor ratio. To make a voltmeter, an Arduino is connected in parallel with one resistor, and the large resistance (the divider) scales the input voltage down to a measurable range. This principle allows the built voltmeter to measure different voltage ranges accurately without damaging the components.
Multimeter in Voltage Mode

## Slide 5
Components
Arduino UNO
Breadboard
16*2 LCD Display
LED Bulb
Potentiometer (10k)
Jumper Wire (M-F and M-M)
Resistor (220, 10k, 100k)

## Slide 6
Arduino Uno R3 | Resistor | LED(Red) | LCD | Potentiometer
7 | 220 | (+)ve |  | 
8 |  |  | RS | 
9 |  |  | E | 
10 |  |  | DB4 | 
11 |  |  | DB5 | 
12 |  |  | DB6 | 
13 |  |  | DB7 | 
5V | 220 |  | BLK, VCC | (+)ve
GND |  | (-)ve | RW, BLA, GND | (-)ve
A0 | 10K(-), 100K(+) |  |  | 
 |  |  | V0 | MIDDLE TERMINAL
Connections

## Slide 7
Circuit Diagram

## Slide 8
Mechanism
Arduino’s analog input pins (A0–A5) can only measure voltages from 0 to 5 V
However, a voltage divider circuit is made of two resistors in series (R1 and R2). The higher voltage is applied across both resistors, and the Arduino reads the voltage across the lower resistor (R2).
Let, Vin is the external voltage to be measured. Vout is the scaled voltage safe for Arduino. The input voltage (Vin) is divided down by the resistor ratio so the Arduino sees only a portion of it.
The Arduino’s ADC (Analog-to-Digital Converter) converts this Vout (0–5V) into a digital value (0–1023 for 10-bit ADC).
In code, the Arduino scales the ADC reading back up using the resistor ratio found by voltage divider law:
​

## Slide 9
Code

## Slide 10
Outcomes
Analog to digital conversion
Calibration of voltage readings
LCD interfacing
Safety in voltage handling
A voltmeter is used in almost all circuits in real life
Without proper voltage measurement, no electrical device can be made
Can be used to prove VDR (Voltage Divider Rule)
Can be used to measure DC voltages up to 50V
Applications in real life

## Slide 11
Future Scope
IoT Integration
Data Logging
AC Measurement
Higher Accuracy
Compact Design

## Slide 12: THANK YOU!